## Slide 1
Bo LU
EEE Department, HKU
Klayout Training v0.1
October 05, 2022

## Slide 2
1. Intro and Installation of Klayout
2. Design with Klayout
3. Collaborate with Python (Not Necessary)

## Slide 3: 1. What is Klayout
Intro to CAD: Computer Aided Design
Technology CAD(TCAD): NEMO5, Silvaco, Synopsys Sentaurus, Lumerical, etc…
EDA: Sinopsis, Mentor, Cadence, Lumerical, Altium Designer, Tanner L-edit, Klayout, etc…
For optoelectronics: LED/Laser/HEMT/GaN-Based Device
Classic tool: L-edit
  Friendly to new user with lots of reference materials
Lack of lic
Use tool from Silicon Photonics: Klayout
  Free, Open Source
  Easy to layout manually
  Active Author in forum
  Be able to layout with ONLY CODE
Layout of Silicon Photonics
Gratings and Bends

## Slide 4: 1. Installation of Klayout
Klayout: https://www.klayout.de/
Author: Matthias Köfferlein (German)
Download:
  Available for Linux, Windows, MacOS
  Documentation:
  User Manual
  Introduction to Script
  API for Code
Forum:
  Leave message to author
  Ask questions in Forum
  Google bugs and get result in Forum

## Slide 5: 2. Introduction of Layout
After installing Klayout: 3 icons
Default mode will be Viewer
  Only for view
  Automatically open *.gds file in this mode
Editor mode
  View, edit and generate
Viewer mode
  Only for view
Change Default to Editor mode:
  Caution !!! Be careful with your design
  Open Klayout, File --> Setup
  Setup --> Editing mode
  tick Use editing mode by default
icons
Viewer mode
Editor mode
Setup 1
Setup 2

## Slide 6: 2. Introduction of Layout
Before Using Klayout:
Before Layout
  Setup Universal Layer property (Strongly recommend in Group)
    e.g. For Mesa Etch Mask, LU Bo use Green Color in layout, Others use Yellow Color. The layout could still be recognized but need more time.
  Tools --> Manage Technologies
  Technology Manager --> General --> Layer Properties
  Load file here
More readable file (Excel) will be released for everyone editing soon.
Mesa
CSL
Mesa
CSL
Excel fig insert here soon

## Slide 7: 2. Introduction of Layout
Start Using Klayout:
Layout Tools
  Select: select for an object. e.g. Cell, Box, Device you draw
    Press ESC back to select. F2 back to main filed (Fn+F2 if hotkey is occupied)
  Move: Move the object you select. Strongly recommend:
    Select Object First
    Then click Move Button
    Finally, use keyboard to move the object
  Ruler: Measure the length
    Ruler mode: Use your mouse determining the length
    Measure mode: Automatically get the length
    Ctrl+K clear all rulers in the layout
  Box: Create object
    Select a layer first, Click Box Button and Draw in the area you want
    ESC, Double click the Object you created, view and edit the properties

## Slide 8: 2. Introduction of Layout
Start Using Klayout:
Layout Panel
  Create a New File
    File --> New Layout, then OK
  Cells Hierarchy in left panel
  Layer Properties in right panel
    If no layer shows here, right click in layer panel
    Untick Hide Empty layers
    Need to add new layer:
      Add in the layer properties file
      Everyone can share the new layer you setup
    If need to add new layer manually:
      Edit --> Layer --> New Layer
      Input Layer and Datetype
      File --> save layer properties, then you can share it
  Coordinate at right bottom

## Slide 9: 2. Introduction of Layout
Start Using Klayout:
Layout Panel
  Cell Array (important)
    Only [TOP cell] at the beginning
    Edit --> New cell [Box]
    Draw 50x50 rectangle in [Box] (Reminder: Use Box in Page6), then back to [TOP], right click --> Show As New Top
    To insert [Box] in [TOP], [TOP] Show As New Top, double click [Box] to hide it, drag it into the draw panel of [TOP]
    Double click the object in [TOP], set properties, e.g. array
    Double click [Box] to unhide it

## Slide 10: 2. Introduction of Layout
Start Using Klayout:
Change Layer of Object
  Select Object
  Select the layer will be transferred
  Edit --> Selection --> Change Layer

## Slide 11: 2. Introduction of Layout
Start Using Klayout:
Boolean Operation
  Select Objects in different layers
  Edit --> Layer --> Boolean Operations
Moved apart

## Slide 12: 2. Introduction of Layout
Start Using Klayout:
XOR tool
  File --> Open in same panel
  Tool --> XOR tool
  Save as file and share to others

## Slide 13: 2. Introduction of Layout
Conclusion:
Change Default Mode to Editor if you like, just be careful with your design
Setup layer properties first for convenient group communication
ESC back to select, F2 back to main field
Coordinate at right bottom
Move function: Select --> Move --> Keyboard moving
Ctrl+K clear all rulers in the layout
Show, Hide and Add layer properties
Create Cell Array follow the guidance
Readable file (Excel) for managing the layer properties will be released soon
  everyone can access this excel file and then execute the run.bat file to generate a new file for group use.
  Bugs/Issues about the Slides/lyp file can be reported and updated in Wechat group or Github here

## Slide 14: 3. Collaborate with Python
Klayout has 2 modes for Coding:
Python code individually
Ruby code embedded
Here introducing Python only, go to official website for ruby
Install Python
Install Package Klayout
Start using Python Script
Example by LU Bo
  More details about this part will be released if needed, contact in Wechat group or Github here

## Slide 15: Thank You!